DHS: Seniors and People with Disabilities

State Operated Community Program

SOCP Nurse Tools: http://www.dhs.state.or.us/spd/tools/dd/socp/nurses.html

Oxygen Concentrators – operational instructions

An oxygen concentrator is a machine that separates oxygen from nitrogen in the air, concentrates it and delivers it to a client at a prescribed flow rate.

It is very important to follow the prescribed level of oxygen flow. Do not increase or decrease the flow without a physician’s order.

The following items should be available when using an oxygen concentrator:

- Cannula and tubing

- Back-up oxygen cylinder, and regulator with base or card (in case of power failure).

- If the concentrator fails, it will be replaced by the company who it is rented from.

- Concentrators are checked in their place of service for function every 60, 90, or 120 days depending on the manufacturer and the provider of the machine.

Placement of concentrator:

- Position the concentrator near an electrical outlet where it can be centrally located for client daily activities

- Position the unit away from curtains or drapes, hot air registers, heaters and fire places.

- Be sure to place the unit so that each side is a least 12 inches from a wall or other obstruction.

- Do not place the unit in a confined area.

- Do not place concentrator on deep pile carpet which may lead to overheating.

Turning ON the concentrator/oxygen:

- Plug the concentrator into a properly grounded electrical ground outlet. DO NOT use an extension cord or power strip.

- Turn the switch to the “ON” position.

- Adjust the flow adjustment knob until the flow meter registers the prescribed flow rate.

- Attach the tubing from the cannula to the oxygen outlet.

- Put the cannula or mask on the client and adjust for comfort.

Turning OFF the concentrator / oxygen:

- Remove the nasal cannula or mask.

- Turn the concentrator power switch to the “OFF” position.

- It is not necessary to turn the flow control off once it has been set properly. However, it should be checked each time the concentrator is turned on.

Cleaning and maintenance:

- DO NOT operate concentrator WITHOUT CABINATE FILTER in place.

- On a weekly basis, wash the cabinet filter, usually located in the back of the unit.

- Remove filter and wash in a solution of warm soapy water.

- Rinse the filter thoroughly, and dry with a soft absorbent towel.

- Replace the filter.